## Slide 1: Computer architecture
Mini project
2018503512

## Slide 2: Bcd to 7 segment code
n Binary Coded Decimal (BCD) encoding scheme each of the decimal numbers(0-9) is represented by its equivalent binary pattern(which is generally of 4-bits).
Whereas, Seven segment display is an electronic device which consists of seven Light Emitting Diodes (LEDs) arranged in a some definite pattern (common cathode or common anode type), which is used to display Hexadecimal numerals(in this case decimal numbers,as input is BCD i.e., 0-9)

## Slide 3: Example for Bcd to seven segment code
Display | D | C | B | A | a | b | c | d | e | f | g
0 | 0 | 0 | 0 | 0 | 1 | 1 | 1 | 1 | 1 | 1 | 0
1 | 0 | 0 | 0 | 1 | 0 | 1 | 1 | 0 | 0 | 0 | 0
2 | 0 | 0 | 1 | 0 | 1 | 1 | 0 | 1 | 1 | 0 | 1

## Slide 4: BCD to gray code
A Gray code is an encoding of numbers so that adjacent numbers have a single digit differing by 1. The term Gray code is often used to refer to a "reflected" code, or more specifically still, the binary reflected Gray code.

## Slide 5: Example:
S.NO | BCD | Gray Code
1 | 0000 | 0000
2 | 0001 | 0001
3 | 0010 | 0011

## Slide 6: Bcd to excess 3
The excess-3 code (or XS3) is a non-weighted code used to express code used to express decimal numbers. It is a self-complementary binary coded decimal (BCD) code and numerical system which has biased representation.

## Slide 7: example
s.no | bcd | Excess 3
1 | 0000 | 0011
2 | 0001 | 0100
3 | 0011 | 0110

## Slide 8: Code:
.data
promptmsg: .asciiz "\nEnter the BCD number bit by bit:\n"
errormsg: .asciiz "\n!!!Enter input bit by bit!!!!\n"
newline: .asciiz "\n"
space: .asciiz " "
horizontal: .asciiz " -- "
vertical: .asciiz "|"
seven_segment: .asciiz "SEVEN SEGMENT DISPLAY "
longspace: .asciiz " "
excess_3: .asciiz "EXCESS-3 CODE"
grey_code: .asciiz "GRAY CODE"
s1: .asciiz " "
s2: .asciiz " "
.align 4
print: .space 28
bcd_invalid: .asciiz "\nTHIS IS NOT A BCD number \n Enter valid input!!!"
A: .asciiz "a:"
B: .asciiz "b:"
C: .asciiz "c:"
D: .asciiz "d:"
E: .asciiz "e:"
F: .asciiz "f:"
G: .asciiz "g:"
.align 4
array1: .space 20

## Slide 9: Obtaining input and verifying it
.text
re:
# displaying prompt message
li $v0,4
la $a0,promptmsg
syscall
# counter
addi $t0,$zero,0
# getting user input
while:
beq $t0,16,exit
flag2:
li $v0,5
syscall
# input verification
bgt $v0,1,flag1
blt $v0,0,flag1
# storing input in array
sw $v0,array1($t0)
add $t0,$t0,4
j while
exit:
#-taking from
li $t0,12
lw $t1,array1($t0)
move $s3,$t1
li $t0,8
lw $t1,array1($t0)
move $s2,$t1
li $t0,4
lw $t1,array1($t0)
move $s1,$t1
li $t0,0
lw $t1,array1($t0)
move $s0,$t1
beq $s0,1,verify
correct:

## Slide 10: Segment-1
li $t0,0
#-7 segment
li $v0,4
la $a0,seven_segment
syscall
li $v0,4
la $a0,newline
syscall
#-segment 1
li $t2,1
sub $t3,$t2,$s1
sub $t4,$t2,$s3
and $t5,$t3,$t4
or $t5,$t5,$s2
and $t6,$s1,$s3
or $t5,$t6,$t5
or $t5,$t5,$s0
li $v0,4
la $a0,newline
syscall
li $v0,4
la $a0,A
syscall
li $v0,1
move $a0,$t5
syscall
sw $t5,print($t0)
addi $t0,$t0,4

## Slide 11: Segment 2 Segment 3
#-segment 2
sub $t3,$t2,$s2
sub $t4,$t2,$s3
sub $t5,$t2,$s1
and $t6,$t3,$t4
or $t6,$t6,$t5
and $t7,$s2,$s3
or $t6,$t6,$t7
li $v0,4
la $a0,space
syscall
li $v0,4
la $a0,B
syscall
li $v0,1
move $a0,$t6
syscall
sw $t6,print($t0)
addi $t0,$t0,4
#-segment 3
sub $t3,$t2,$s2
or $t3,$t3,$s3
or $t3,$t3,$s1
li $v0,4
la $a0,space
syscall
li $v0,4
la $a0,C
syscall
li $v0,1
move $a0,$t3
syscall
sw $t3,print($t0)
addi $t0,$t0,4

## Slide 12: Segment 4 Segment 5
#-segment 4
sub $t3,$t2,$s1
sub $t4,$t2,$s2
sub $t5,$t2,$s3
and $t6,$t3,$t5
and $t7,$t3,$s2
and $t8,$s1,$t4
and $s4,$t8,$s3
and $t9,$s2,$t5
or $t6,$t6,$t7
or $t6,$t6,$s4
or $t6,$t6,$t9
or $t6,$t6,$s0
li $v0,4
la $a0,space
syscall
li $v0,4
la $a0,D
syscall
li $v0,1
move $a0,$t6
syscall
sw $t6,print($t0)
addi $t0,$t0,4
#-segment 5
sub $t3,$t2,$s1
sub $t4,$t2,$s3
and $t5,$t3,$t4
and $t6,$s2,$t4
or $t5,$t5,$t6
li $v0,4
la $a0,space
syscall
li $v0,4
la $a0,E
syscall
li $v0,1
move $a0,$t5
syscall
sw $t5,print($t0)
addi $t0,$t0,4

## Slide 13: Segment 6 Segment 7
#-segment-6
sub $t3,$t2,$s2
sub $t4,$t2,$s3
and $t5,$t3,$t4
and $t6,$s1,$t3
and $t7,$s1,$t4
or $t5,$t5,$t6
or $t5,$t5,$t7
or $t5,$t5,$s0
li $v0,4
la $a0,space
syscall
li $v0,4
la $a0,F
syscall
li $v0,1
move $a0,$t5
syscall
sw $t5,print($t0)
addi $t0,$t0,4
#-segment-7
sub $t3,$t2,$s1
sub $t4,$t2,$s2
sub $t5,$t2,$s3
and $t6,$t3,$s2
and $t7,$s1,$t4
and $t8,$s1,$t5
or $t6,$t6,$t7
or $t6,$t6,$t8
or $t6,$t6,$s0
li $v0,4
la $a0,space
syscall
li $v0,4
la $a0,G
syscall
li $v0,1
move $a0,$t6
syscall
sw $t6,print($t0)
addi $t0,$t0,4

## Slide 14: Displaying segments
#-SEGMENT DISPLAY
li $v0,4
la $a0,newline
syscall
li $t0,0
lw $t1,print($t0)
beq $t1,1,segment1
f1:
li $v0,4
la $a0,newline
syscall
li $t0,20
lw $t1,print($t0)
beq $t1,1,segment2
beq $t1,0,space1
f2:
li $v0,4
la $a0,space
syscall
li $t0,4
lw $t1,print($t0)
beq $t1,1,segment3
f3:
li $v0,4
la $a0,newline
syscall
li $t0,24
lw $t1,print($t0)
beq $t1,1,segment4
f4:
li $v0,4
la $a0,newline
syscall
li $t0,16
lw $t1,print($t0)
beq $t1,1,segment5
beq $t1,0,space2
f5:
li $v0,4
la $a0,space
syscall
li $t0,8
lw $t1,print($t0)
beq $t1,1,segment6
f6:
li $v0,4
la $a0,newline
syscall
li $t0,12
lw $t1,print($t0)
beq $t1,1,segment7
f7:
li $v0,4
la $a0,newline
syscall

## Slide 15: Excess-3 Code
#-Excess-3 code
li $v0,4
la $a0,newline
syscall
li $v0,4
la $a0,excess_3
syscall
li $v0,4
la $a0,newline
syscall
li $t2,1
#**w**
and $t1,$s1,$s2
and $t3,$s1,$s3
or $t4,$s0,$t1
or $t5,$t4,$t3
li $v0,1
move $a0,$t5
syscall
#*x*
#b'c+b'd+bc'd'
sub $t1,$t2,$s1 #b'
sub $t3,$t2,$s2 #c'
sub $t4,$t2,$s3 #d'
and $t5,$t1,$s2
and $t6,$t1,$s3
and $t7,$s1,$t3
and $t8,$t7,$t4
or $t9,$t5,$t6
or $s5,$t9,$t8
li $v0,1
move $a0,$s5
syscall
#*y*
#cd+c'd'
sub $t1,$t2,$s2
sub $t3,$t2,$s3
and $t4,$s2,$s3
and $t5,$t1,$t3
or $t6,$t4,$t5
li $v0,1
move $a0,$t6
syscall
#*z*
#d'
sub $t1,$t2,$s3
li $v0,1
move $a0,$t1
syscall

## Slide 16: Grey Code
#--GREY--code
li $v0,4
la $a0,newline
syscall
li $v0,4
la $a0,newline
syscall
li $v0,4
la $a0,grey_code
syscall
li $v0,4
la $a0,newline
syscall
#*g0*
li $v0,1
move $a0,$s0
syscall
l
#*g1*
xor $t1,$s0,$s1
li $v0,1
move $a0,$t1
syscall
#*g2*
xor $t1,$s1,$s2
li $v0,1
move $a0,$t1
syscall
#*g3*
xor $t1,$s2,$s3
li $v0,1
move $a0,$t1
syscal

## Slide 17: Functions:
#- END
li $v0,10
syscall
# ERROR MSG
flag1:
li $v0,4
la $a0,errormsg
syscall
j flag2
segment1:
li $v0,4
la $a0,horizontal
syscall
j f1
segment2:
li $v0,4
la $a0,vertical
syscall
j f2
segment3:
li $v0,4
la $a0,vertical
syscall
j f3
segment4:
li $v0,4
la $a0,horizontal
syscall
j f4
segment5:
li $v0,4
la $a0,vertical
syscall
j f5
segment6:
li $v0,4
la $a0,vertical
syscall
j f6
segment7:
li $v0,4
la $a0,horizontal
syscall
j f7

## Slide 18
space1:
li $v0,4
la $a0,s1
syscall
j f2
space2:
li $v0,4
la $a0,s2
syscall
j f5
verify:
add $t1,$s1,$s2
bgt $t1,0,invalid_input
j correct
invalid_input:
li $v0,4
la $a0,bcd_invalid
syscall
j re

## Slide 19: FLOW OF CODE:
start
Read BCD no.
Calculate 7 segments
Calculate Gray Code
Calculate excess-3
Print 7 segments
Print excess-3
Print Gray Code
End

## Slide 20: MIPS ARCHITECTURE

## Slide 21: Output:

## Slide 22
THANK YOU